## Slide 1: Bing Maps Private Cloud
Parallel Processing on the Prairie
31-Jul-2013

## Slide 2: BITs Product Summary
Graz, Austria
UltraCam development
Commercial software
Computer vision research
Boulder, Colorado
Bing Maps data center
Software development
Acquisition management
Steve Stanzel, IPE GeoSpatial Program Manager
Streetside
UltraMap
UltraCamM
UltraCamP
UltraCam Aerial
Global Ortho
Oblique
Vectors
TERRESTRIAL
AERIAL

## Slide 3: Global Ortho
Largest Aerial Mapping Project in Industry History
Complete Coverage US (“Lower 48”)
12 European Markets
10,400,000 square km
Order of Magnitude Cost Reductions:
USGS Program  10 years; 50cm
Bing Program  2.5 years; 30cm
24 months initial acquisition
238 terapixels, ~1.2 petabytes
UltraCamG (Giant)
Largest format aerial mapping camera
8 lenses, 14 CCDs, 28 HDDs
Pan, color, IR
28K pixel swath, 252M pixels total
417 MB / capture event
2.3 million collected to date
Ortho, Elevation, Classification
Exclusive to Clear 30 project
Notes: Caveats on numbers

## Slide 4: UltraCam Tech
UltraCam Xp (Large Format)
Simultaneously collects Pan, R,G,B, near infrared (NIR)
Panchromatic image size 17,310 x 11,310 pixels
Color and NIR image size 5,770 x 3,770 pixels
14 6μm CCD’s and 8 precision lenses
14 embedded computers managing 3 Gbits of throughput to 14 redundant drives
Approximately 6,600 uncompressed images per data storage unit (~4.2 TB)
11 hours of collection time per single data unit at typical speeds and flight lines
Image geometric accuracy is approximately +/- 0.002mm
Mobile Server, high capacity storage on the ground

## Slide 5: UCG Custom Aerial Camera for Global Ortho
~9 km
Largest footprint of all camera systems
~6 km

## Slide 6: UCG image @ full resolution (Vatican City)
Grayscale
Infrared

## Slide 7: Global Ortho Processing
Data Collection
  Build Cameras
  Partner with Fliers
  1PB imagery
Aerial Triangulation
  UMAT
  Ground Control
Radiometry Processing
  Haze Removal
  Sun Hotspot Removal
  Tone Balancing
Ortho Rectification
  Re-project Images
Mosaicing
  Define Seam Lines
  Apply Seam Lines
  Apply Color Corrections
  Seam Line Blending
Export
  Re-project To Output Formats
  Copy to EHDs and ship

## Slide 8: Radiometry Examples

## Slide 9: Other things we do:
DSM, DTM, Classification
Bird’s Eye & Synthview
Streetside
Notes: “Cowhide” – extraction of additional value or revenue from imagery assets.

## Slide 10: We match pan images to get DSMs
Oakland
San Francisco
Richmond, VA
Notes: Stereomatcher run on multiple stereo-pairs and results are fused together

## Slide 11: We classify buildings, craters, vegetation, water, …
Notes: Left image shows high-slope areas in grey, red/pink shows building centers, other colors = ground-level
Right image shows classification results from PCVLib

## Slide 12: Using DSM and classification, we extract a DTM
Richmond, VA
Los Angeles, CA
Notes: Ortho DTM is then used to ortho-rectify imagery for delivery to DG

## Slide 13: Bird’s Eye / Oblique Imagery

## Slide 14: Re-projected Ortho
N
N

## Slide 15: SynthView Processing Steps
15
1. Orthorectification
2. Seam line detection
3. Ortho inset
4. Color balancing
5. 3D models

## Slide 16: Streetside
5th 6th generation sensor 54 mp/capture event
Panoramic camera, LIDAR, GPS, IMU, DMI
4th generation user experience
Silverlight-based “cube” viewer
Simplified geometry

## Slide 17: 9 Distinct Data Products
1. Panoramic imagery
2. Raster depth map
3. Simplified geometry
4. Privacy masks
5. Low-rez thumbnail
6. Tiled vector data for overlays
7. Event-to-vector mapping
8. Coverage overlays
9. Geopositioning metadata

## Slide 18: Image Processing Framework
Our “Map/Reduce” framework that parallelizes our image processing algorithms across our 23k cores and 72 petabytes of storage

## Slide 19: Big Data
Software as a Service (SaaS)
  Examples of SaaS include: Google Apps, Quickbooks Online and Salesforce.com
Platform as a Service (PaaS)
  Examples of PaaS include: Amazon Elastic Beanstalk, Heroku, EngineYard, Google App Engine, and Microsoft Azure
Infrastructure as a Service (IaaS)
  Examples of IaaS include: Amazon CloudFormation (and underlying services such as EC2), Rackspace Cloud, Google Compute Engine, and RightScale
Image Processing Framework
BIT Compute
Our “Map/Reduce” framework that parallelizes our image processing algorithms across our 23k cores and 72 petabytes of storage

## Slide 20: The Big Picture
MS
GFS
Data
Center
Flyers &
Data
Capture
Vendors
Image
Processing
Framework
Image
Publishing
System
Ingest
Publish
Update
Stitch
Files
Imagery
Meta
Data
Files
Drop
Specs

## Slide 21: What is the IPF?
Parallel Processing Framework and GeoSpatial metadata store
  Manages up to “N” 2000-ish multi-core node “Clusters” cooperating to produce an answer
  Multi-Petabyte redundant (3 copies) storage system
  Standard Windows/.NET APIs to read/write data files
  Data files can be versioned and have commit/rollback semantics
  Meta-data repository of geo-spatial data
  Supports automatic (headless) and manual (interactive) processing
  Can execute scripts (powershell, .bat, etc), console apps, and GUI apps (manual only)
  Implements “Data flow parallelism” through the disk system, i.e. no MPI support
  Degree of parallelism and parallel data flow is 100% programmable
  Data warehouse of coverage and tile usage
Comparable Systems:
Google’s Map/Reduce
Yahoo’s Hadoop
Windows High Performance Cluster
OSD’s Cosmos
Investment:
37 person-year investment, begun in 2006
100% C#/.NET implementation
Current team of 1 Lead, 3 Devs

## Slide 22: IPF Processing Concepts
Pipeline – the logical graph of parallel operations
Process – a suite of separate parallel operations that execute serially
Step – a specific logical operation within a Process
Task – a single executing Package of a step
Package – a PowerShell script and programs it invokes
Job – a Pipeline Version processing a data-set
JobStart
Process B
Step B1
Step B2
Step B3
Process C
Step C1
Step C2
Process D
Step D1
Step D2
Sample
Pipeline
Initial
Plan
Step
D3

## Slide 23: Streetside Intermediate Pipeline

## Slide 24: BITs Operator Console – Web UI

## Slide 25: BITs Pipelines

## Slide 26: IPF Summary
Asymmetric Directed Graph defines parallel plan
  Multiple Tasks within a Step run in parallel
  Steps within a Process proceed sequentially
  Non-dependent Processes execute in parallel
  User written task “planners” enable fine grain control of the plan to IPF pipeline developers
  Manual steps incorporate human operator interaction within the graph
IPF Managed Storage
  3 replicas on separate nodes for availability/reliability/performance
  File versioning system to automate logical updates
  Geo-Spatial metadata repository in SQL
JobStart
Initial
Plan
Process B
Step B1
Step B2
Step B3
Process C
Step C1
Step C2
Process D
Step D1
Step D2
Step D3
Sample
Pipeline

## Slide 27: Container-Based Compute and Scalable Data Production

## Slide 28: Container-Based Compute, Longmont, CO
MICROSOFT CONFIDENTIAL
28
Designed for Efficiency & Rapid Deployment
8 acres (1 developed)
4 modules per deployment area
3 deployment areas populated
Power for up to 13 deployment areas:
55 modules, 290,400 Cores, 968PB storage
Dell hi-efficiency modules
1.03PUE (1.9 industry average, 1.13 Google average)

## Slide 29
DELL Containers
Arriving in Longmont
April 17th 2011

## Slide 30
This man really trusts
the crane operator!

## Slide 31
DELL Compute/Storage
Container
Transformer & UPS
Air Flow Vents

## Slide 32
Inside a DELL Container
Compute Rack
2 “Side by Side” Servers
Disk Sled Rack
Disk Sled Rack
On the truck
At DELL’s Austin Plant

## Slide 33: Cluster Compute Core Utilization
 |  |  |  | Rule, Instance, Object | Scale | Sample Count | Min Value | Max Value | Average Value | Standard Deviation
 |  |  |  | Processor % Processor Time Total 2008 | 1 | 70407587 | 0 | 100 | 52.85 | 20.96
Notes: Add MapImpress
Add util graph from Brad
Add SQL stats

## Slide 34: InfiniBand Network: Current C20 topology (1320 nodes)
30-servers
30-servers
30-servers
30-servers
30-servers
30-servers
Rack 5
30-servers
30-servers
30-servers
Rack 10
30-servers
30-servers
30-servers
Rack 15
L2 - #10
L2 - #5
L2 - #1
L2 - #15
= 6 QDR L2 to L3 links
= 2 QDR L1 to L2 links
L1
L3
L2
Counts:
L1: 46
L2: 15
L3: 9
L1
L2
L3
IS5030 Mellanox ($5.6k)
Grid Director 4036E $19.9k
Notes: L1 and L2 are IS5030 $5.6k / switch
L3 is 4036E “Grid Director” 34 port IB to 10GigE Ethernet that also serves as gateway to our Verari gear.

## Slide 35: BITs by the Numbers
Statistics on BITs Processing

## Slide 36: Daily Statistics E-mail

## Slide 37: Infrastructure Stats

## Slide 38: BITs by the Numbers
Capacity
2,304
Servers
23,538
Cores
53,800
Disks (72 PB)
Data Created Last Year
86.7 TB
Average
Per Day
31 PB
1.5 billion Files
Record
Week
4 PB
56 million
Files
8.7 million Files
Record
Day
363k Files
Per Hour
8.7 million
Files
19 TB
Per Hour
Task
Counts
172k
Per Day
63 million
Last Year
.5 GB
Created
Per Task

## Slide 39: Thanks!
“Golden Spike” Image completing US acquisition on Aug 29 2012 - Boulder Colorado

## Slide 40: Questions?
Thanks for visiting BITs !